## Slide 1
University: University Ferhat Abbas – Sétif1
Institute : science and Technology
Department : Electrotechnique
OPTION : MASTER IN AUTOMATIC CONTROL
Mini-project :
Par : MESSAI Oussama
:MESSAI Oussama
Supervisor : Dr. MOKEDDEM D.

## Slide 2
- Introduction to microcontrollers
- Arduino uno kit with ATmega328p microcontroller
- Ultrasonic sensor HC-SR04
- Automatic door system with LED ( electronic circuit )
- Function mode
- The Tasks
- Arduino programming Code
- Comment or Conclusion

## Slide 3
Introduction :
Microcontroller is a small computer on a single integrated circuit containing
a processor core, memory, and programmable input/output peripherals.
Program memory in the form of Ferroelectric RAM .
Microcontrollers are used in automatically controlled products and
devices, such as automobile engine control systems, implantable
medical devices, remote controls, office machines, appliances, power
tools, toys and other embedded systems.

## Slide 4
Arduino uno kit with ATmega328p microcontroller :
The Arduino Uno is a microcontroller board based on the ATmega328 It
has 14 digital input/output pins (of which 6 can be used as PWM
outputs), 6 analog inputs, a 16 MHz ceramic resonator, a USB
connection, a power jack, an ICSP header, and a reset button. It
contains everything needed to support the microcontroller; simply
connect it to a computer with a USB cable or power it with a AC-to-DC
adapter or battery to get started.

## Slide 5
Microcontroller ATmega328
Operating Voltage 5V
Input Voltage (recommended) 7-12V
Input Voltage (limits) 6-20V
Digital I/O Pins 14 (of which 6 provide PWM output)
Analog Input Pins 6
DC Current per I/O Pin 40 mA
DC Current for 3.3V Pin 50 mA
Flash Memory 32 KB (ATmega328) of which 0.5 KB used by bootloader
SRAM 2 KB (ATmega328)
EEPROM 1 KB (ATmega328)
Clock Speed 16 MHz
Length 68.6 mm
Width 53.4 mmS

## Slide 6
Ultrasonic Sensor :
Ultrasonic ranging module HC - SR04 provides 2cm - 400cm non-contact
measurement function, the ranging accuracy can reach to 3mm. The
moduleincludes ultrasonic transmitters, receiver and control circuit.
The basic principle of work :
(1) Using IO trigger for at least 10us high level signal,
(2) The Module automatically sends eight 40 kHz and detect whether there is a
pulse signal back.
(3) IF the signal back, through high level , time of high output IO duration is
Electric Parameter :
Working Voltage DC 5 V / Working Current 15mA
Working Frequency 40Hz
Max Range 4m / Min Range 2cm
MeasuringAngle 15 degree
the time from sending ultrasonic to returning

## Slide 7
- 5V Supply
- Trigger Pulse Input
- Echo Pulse Output
- 0V Ground
Electric Parameter :
Working Voltage DC 5 V / Working Current 15mA
Working Frequency 40Hz
Max Range 4m / Min Range 2cm
MeasuringAngle 15 degree

## Slide 8
Timing diagram :
The Timing diagram is shown below. You only need to supply a
short 10uS pulse to the trigger input to start the ranging, and then the module
will send out an 8 cycle burst of ultrasound at 40 kHz and raise its echo. The Echo
is a distance object that is pulse width and the range in proportion .You can
calculate the range through the time interval between sending trigger signal and
receiving echo signal. Formula: uS / 58 = centimeters or uS / 148 =inch; or: the
range = high level time * velocity (340M/S) / 2; we suggest to use over 60ms
measurement cycle, in order to prevent trigger signal to the echo signal.

## Slide 9
Automatic door system with LED ( electronic circuit ) : this is
the circuit of our system realized with LED instead of DC motor
The concept still the same .

## Slide 10
Function mode: we have three Modes in this simple system we
can divide to Cycle, Event and Mixt
Cycle : Sending periodic signal over and over from trig OUTPUT
Event : Waiting for the signal return, receiving from echo INPUT
Mixt : sending and receiving the signal , And display the
distance on LED also play a sound if obstacle was detected

## Slide 11
The Tasks :
First Tasks : #1 Measure the distance and display it on the Red
LED
Second tasks : #2 Detect the obstacle (human) under 50cm of
distance and open the door or power on the green LED
How it’s work ?
When the distance measured is less than 50cm means that
there is obstacle in the range of 0-50 cm from the ultrasonic
sensor ( door )
N.B : I added the buzzer parallel with the green LED

## Slide 12
The Programme :

## Slide 13
Arduino is intended for use by both non-technical people with no previous programming experience , So any one of You can realize useful project using this Kit 
a lot of ideas in your head that you can make them come true in easily way with some component , even that you are not proficient electronic circuit.
Comment : ( Conclusion )
Waiting For Your Projects :P 

## Slide 14
Any Questions ? 
Thank You